## Slide 1
NTT’s Label Switching VPN “Label VPN” Overview
April 13, 2000
LION-WP1 meeting
NTT Confidential Proprietary

## Slide 2
What is GMN-CL?
Electrum Cyber Society (ECS)
- Cyber Space
- Cyber Software
Mega-media Network (GMN)
Target is
- Multimedia network service of
10 Mbits transfer per second,
- Price is 10,000 yen per month,
- Realizing until the year 2005.
Photonic Network
Innovative NTT R&D
towards 21st century
GMN : Global Megamedia Networks
GMN-CL : ConnectionLess Networking Technologies for GMN
GMN-CL
The first step towards the Mega-media World.
・Label switching
・VPN (Virtual Private
Network) support.
・QoS (Quality of Service)
guarantee
・Multicast
･ ･ ･ ･ ･
[Application]
[Network Service]
[Infrastructure]

## Slide 3
ATM Network
GMN-CL (Label Switching Technology of NTT) Architecture
Edge Node
QoS：Quality of Service MC：Multicast
VPN：Virtual Private Network VPN-ID：VPN Identifier
・・・
VPN
Server
MC
Server
QoS
Server
Route
Server
Servers for advanced services
IP Packet
IP address
aa.bb.cc.dd
IP Packet
IP address
aa.bb.cc.dd
Core encapsulating
technology
Forwarding
control system
Routing control system
Core Network
Core
Transfer
Node
IP
address
xxx-yyy
Core Packet
Core Header
Management Network
Edge Node
Forwarding Control System :
High-speed & Efficient Forwarding by Implementing Core Protocol
Routing Control System :
Efficient Distribution of Routing Tables by Central Processing
Core
Transfer Node
・Core Address
(Forwarding Label)
・VPN-ID
・QoS class

## Slide 4
Core encapsulation for various services
Core Network
IP address
aa.bb. cc.dd
Core Protocol
IP
address
Core header
Encapsulation
xxx-
yyy
xxx-
yyy
aa.bb. cc.dd
aa.bb.
cc.dd
IP
address
Core header
Decapsulation
xxx-
yyy
Access Network
Edge Node
(EN)
Core Layer as an intermediate layer between IP and ATM enables
(1)various services
(2)multiprotocol support
Core Packet
IP Packet
Core Packet
IP Packet
IP address
Edge Node
(EN)
Access Network
User
Network
User
Network
Core Header
・Core Address
(Forwarding Label)
・VPN-ID
・QoS class

## Slide 5
Core Encapsulation and Layer
IP packet
Len
CRC-32
LLC/SNAP
CORE
Last cell
First cell
(Core cell)
IP packet
AAL5-CPCS PDU
Core header
Cell sending direction
IP:
Core:
AAL5/ATM
:

## Slide 6
ATM
ATM
ATM
ATM
TDP/
IP Ｎａｖｉ
IP
IP
IP
IP
Core packet forwarding
IP packet
・IP Navigator/Tag Switching
IP packet
ATM cell
ATM cell
ATM cell
Label for transferring (VPI/VCI)
TDP/
IP Ｎａｖｉ
TDP/
IP Ｎａｖｉ
TDP/
IP Ｎａｖｉ
IP packet
IP packet
・GMN‐CL
IP
IP
ATM
ATM
ATM
ATM
CORE
CORE
CORE
CORE
frame
Succeeding cells other than the first cell
Label for transferring (Core address)
Succeeding cells other than the first cell

## Slide 7
ATM connection setup between edge nodes before communication
Cf. Connection Oriented
ATM SW
ATM SW
Signalling, etc.
Core Network
ATM Connection Mode between Edge Nodes
No ATM connection setup between edge nodes
GMN-CL: Connection Less
Edge Node
Transfer
Node
Core Network
Local VCs
（Terminated at Transfer node）
Transfer
Node
Edge Node
Edge Node
Transfer
Node
Transfer
Node
Edge Node
Direct VC connection

## Slide 8
IP
ATM
ATM
Routing Control System
RS
DF
Routing Control Packet
Label Distribution of GMN-CL
Edge Node
Route Calculation
CN
（Core Transfer Node）
CN
（Core Transfer Node）
Re-direction
（Address resolution）
Forwarding
Control System
Edge Node
Label and FEC binding inform
-ation
NMS
Routing Control Packet
IP
ATM
ATM
CORE
CORE
CORE
CORE

## Slide 9
VPN identification of GMN-CL
User site
Edge Node
Edge Node
● VPN identifier is encapsulated into Core header of each frame in Core Network.
● Edge node recognizes correspondence between VPN identifier and access link.
VPN identifier
Link A
Link B
VPN＃A
VPN＃B
Edge node identifies VPN by link, and judges capacity of data transferring
User site
Link A
Edge node gets the address of destination edge node by looking up table for the VPN, adds VPN id., and transmits packet.
Address of destination edge node
Link B
User site
User site
Link １
Link ２
Link １
Link ２
VPN＃A
VPN＃B
Edge node identifies VPN by VPN id., identifies an egress link by a table, and transmits packets.
Core packet
・This id is not read in
ATM layer
・This id is added at upper
layer than ATM in ingress
edge node
Core Network
Address of destination edge node

## Slide 10
Company X
Company Y
Company Z
Customer α
Customer β
Customer γ
Server A
Server B
Server C
Server D
Server E
Server F
Server G
Server H
Server I
Host 1
Host 2
Host 3
Host 4
Host 5
Host 6
Host 7
Host 8
Host 9
VPN-X
VPN-Y
VPN-Z
VPN-α
VPN-β
VPN-γ
VPN by each company
VPN by each
customer
Accessibility from customer α
Accessibility from customer β
Accessibility from customer γ
Server A
Server B
Server C
Host ３
no
no
yes
Host ２
yes
no
To Company X
Server D
Server E
Server F
no
no
yes
no
no
To Company Y
Matrix table of accessibility
CUG-GW (Closed user group - Gate Way)
no
no
Elaborate
Inter VPN Accessibility
Host １
yes
no
no
no
yes
no
From α
CUG-GW

## Slide 11
Advanced IP Connection - QoS Control
Different QoS Classes are Available for Each Customer
Low priority
forwarding
High priority
forwarding
Throughput assurance
for any Input
(1) Minimum Throughput Assured Class
(2) Throughput Preferred Class
(3) Throughput Assured Class
Network Cut-through
Throughput Assured Class
CN
CN
SLT
Minimum throughput assurance
Marking
Non-priority Cells
(for Each PDU)
High Quality
Core Network
Bandwidth
Management Server
Edge
Node
Edge
Node
Core Protocol
Forwarding Layer
Throughput
Preferred Class
Minimum Throughput Assured Class
ATM Network
Overflow
(1)
(2)
(3)
NA
Admission Control
(PCR)
Round-robin
Grouping
Priority Cells (all)

## Slide 12
GMN-CL
Realize streaming services and interactive conferences by high performance hardware multicast
MCRS
MCRS：Multicast route server
Conference hall
Viewer A
Viewer B
Viewer C
Contents provider
High speed Hardware copy
Participation and secession in service
Manages multicast group
Viewer A
Viewer B
Viewer C
Multicast group members
Multicast Service

## Slide 13
Summary
● GMN-CL (NTT) is one of leading implementations of
MPLS VPN
● GMN-CL has advanced features:
- Efficient use of network resources --- Connectionless transport
(Core Layer)
- Elaborate inter-VPN accessibility control --- CUG-GW
- QoS Control, Multicast
Notes: Summary.
In the background where IP-VPN is required, three types of thechnology have been developping.
In these technologies, label VPN is expected to be applied for constructing extranets.
GMN-CL is one of leading implementations of label VPN, and has several enhanced functionalities. Fro example,
Elaborate inter VPN access control by CUG-GW,
Efficient use of network resources by connectionless transport of
Core layer.

## Slide 14
Hardware Forwarding Technology
  No IP-layer forwarding
  Cell Switching (2nd cell, 3rd cell ...)
Edge Node
Core a
1
1
PVP(10)
PVP(6)
PVP(5)
1
Cells→IP Packet
IP Routing
IP Packet→Cells
Cell Forwarding Process
(Core Address lookup)
Cell Forwarding Process
(Cell Forwarding Table lookup)
・・・
Software Forwarding
in IP Layer
Hardware Forwarding
in ATM Layer
・・・
・・・
3
3
3
(Ref.) Small Delay & High-speed Forwarding in Core
Transfer Node
Core Packet
Core
transfer Node
Core Forwarding
Table
Cell Forwarding
Table
：
：
：
：
Core a
VP=5
Core
Address
Output
Route
10
1
10
2
：
：
VP=5
VP=6
：
Output
Route
Input
Route
Packet ID
(VCI)
IP a
1st Cell
2ndCell
1st Cell
2nd Cell
3rd Cell
1st Cell
2nd Cell
Process Sequence in Core transfer Node
•
•
Edge Node
Edge Node