## Slide 1: SDH/SONET Options for Optical Internetworking OIF99-147
®
Presentation Slides
for Contribution OIF99-136
October 19, 1999

## Slide 2: Outline
Optical Internetworking goals
Why SDH based interfaces?
SDH Options
  SDH data interfaces, transparent optical network
  SDH data interfaces, SDH optical network
  Enhanced SDH interfaces for data and optical network
Recommendations
Note: For brevity the term SDH is used here. The intent is to have identical or very similar solutions for both SONET and SDH.

## Slide 3: Goal of Optical Networking
Create a set implementation agreements to foster interoperability of data networking elements over optical networks.
For long haul applications the optical network will use DWDM technology
Due to rapid level of investment, simple, quick to implement solutions are favored
Optical Internetworking is not the OTN!!!

## Slide 4: Possible North American Core Internet
•
•
•
•
•
•
•
Ft. Lauderdale
West Palm Beach
•
X
•
•
•
Albany
Melbourne
Daytona Beach
Raleigh
Fayetteville
•
•
•
•
•
•
Greensboro
•
•
•
Harrisburg
•
•
•
Macon
•
Spartanburg
•
Tallahassee
•
Tampa
Fort Myers
•
Orlando
Pensacola
Mobile
•
•
Birmingham
•
•
Knoxville
Louisville
•
•
South Bend
Durand
•
Lansing
•
•
•
•
Jackson
Minneapolis
•
Des Moines
•
Madison
Topeka
•
Baton Rouge
•
•
Emerson
Colorado Springs
•
•
•
Santa Fe
•
Grand Jct
Salt Lake City
•
Boise
•
•
Reno
•
Yuma
•
Victoria
•
Stockton
•
•
•
Chico
Roseburg
Eugene
•
San Luis Obispo
Atlanta
Nashville
Charlotte
Norfolk
Cleveland
Columbus
Indianapolis
Brampton
Kitchener
Cincinnati
Jacksonville
Philadelphia
New York
Milwaukee
Thunder Bay
Vancouver
Phoenix
Sacramento
Oakland
San Jose
San Francisco
Los Angeles
Austin
Houston
Dallas
Tulsa
Oklahoma City
Chicago
St. Louis
Denver
Portland
Miami
Halifax
London
Detroit
Toledo
Kansas City
San Antonio
El Paso
Fresno
WASHINGTON
Toronto
Pittsburgh
Baltimore
Buffalo
San Diego
Seattle
Omaha
Tucson
Syracuse
Rochester
Hartford
Providence
Boston
Springfield
New Orleans
Richmond
Memphis
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
Portland
•
Manchester
•
Little Rock
•
Shreveport
Albuquerque
Las Vegas
•
4000 km
1500 km
3450 km
2350 km
750 km
950 km
1600 km
900 km
600 km
1300 km
1350 km
750 km
450 km
1250 km

## Slide 5: The clock is ticking….
1999 saw the introduction of line-rate switch and router interfaces
Carriers interconnected them with DWDM, without intervening SDH terminals or ADMs
2000 will see rapid growth of capacity and 10 G router interfaces
Enhanced manageability is needed
The OIF needs to act soon
The SDH rings are gone!

## Slide 6: Suggested early goal for the OIF
Consider long haul network with IP routers directly connected to DWDM transmission, crossing multiple carrier domains
Formulate a set of specifications for configuration, performance and fault management for this situation that can be implemented quickly

## Slide 7: Why the OIF chose to focus on SDH
Carriers operations geared for SDH
Routers use SDH interfaces
DWDM systems with SDH 3R and PM
SDH framers are widely available, with chip volume increasing and prices decreasing
A cost effective interface used by all carriers, available to all suppliers

## Slide 8: The Question-
What does it mean to base Optical Internetworking specifications on SDH framing?

## Slide 9: Option 1: Status Quo
Data elements with SDH interfaces
Optical network provides interconnection, possibly 2R or 3R regeneration
Optical network may provide non-intrusive monitoring for connection verification and performance monitoring

## Slide 10: Option 1: Benefits
3R regeneration in DWDM saves carriers capital, space and power
B1 monitoring helps track down performance problems
J0 section trace verifies connectivity
Continental, global scale networks can be built and monitored

## Slide 11: Option 1: Drawbacks
Non-intrusive PM puts alarm correlation burden on management systems
Lack of AIS generation-
  loss of system visibility during faults
  alarms proliferate on failures
Limited options for protection switching
No direct communications mechanisms between data and optical domains

## Slide 12: Option 2: Standard SDH
Data elements with SDH interfaces
SDH layer termination in optical network
  3R device terminates regenerator section
    B1, J0, regenerator section DCC, AIS
  Configurable device terminates multiplex section
    B2, multiplex section DCC, AIS, RDIs

## Slide 13: Option 2: Benefits
Automatic fault localization
Rapid fault notification
Alarm suppression
Communication channels
More protection switching mechanisms

## Slide 14: Option 2: Drawbacks
Potential for interoperability problems with legacy SDH
Communications channels low bandwidth
Lack of distinct optical layer overheads
Doesn’t address the lack of tandem connection monitoring in the SDH

## Slide 15: Option 3: SDH ++
Several options are possible here, but generally this involves addition of new features supported by SDH overhead bandwidth.
Examples:
  Tandem Connection Monitoring
  High capacity DCC to support modern routing and signaling protocols
  Optical channel identification

## Slide 16: Option 3: Benefits
Removes constraints imposed by current overheads
Makes use of current framers, or requires modest modifications to framer designs
Enables rapid introduction of new features
“Tunnels” through large embedded base of DWDM transmission equipment
Creates independent layer functionality
Rate preserving

## Slide 17: Option 3: Drawbacks
May require framer modifications
Not transparent to legacy SDH traffic

## Slide 18: Recommendations
All three options appear to have applications in service provider networks
  Optical network transparency (Option 1) for legacy networks with proprietary SDH implementations and management
  Standard SDH functionality in optical network (Option 2) for added OAM&P capabilities
  SDH++ (Option 3) for creation of a distinct layer for optical network OAM&P and new embedded operations capabilities

## Slide 19: Recommendations
Propose the OIF architecture document specify three modes of SDH compatible operation, described in this contribution as options 1, 2 and 3
  Equipment supporting option 3 is capable of being software configured to conform with options 2 or 1.
  Equipment supporting option 2 but not 3 is capable of being software configured to support option 1
Contributions sought to further define options