## Slide 1: Label Switching & Lambda Switching
George Swallow
Co-Chair MPLS WG, IETF
Notes: 1

## Slide 2: Label Switching Motivation
Offer benefits of traditionally found only in Level 2 networks directly to IP
  Traffic Engineering, VPNs
Address major network scalability challenges
Permit graceful evolution of routing & services

## Slide 3: Label Switching: Fusing Routing and Switching
Combining:
  Layer 3 routing - scalability and flexibility
  Layer 2 switching - high performance and traffic management
+
or
=
Router
ATM Switch
MPLS Router
ATM MPLS
Router

## Slide 4: MPLS Components
Control component
  Various applications can directly manipulate label bindings
Forwarding component
  Simple label-swapping paradigm
Unicast
Routing
Efficient lookup and forwarding
Per-Label Forwarding, Queuing,
and Multicast Mechanisms
Traffic
Engineering
Virtual
Private
Networks
Frame
Relay
Differentiall
Services
Separation allows flexibility

## Slide 5: Forwarding Component
Simple efficient forwarding
  Label lookup determines output port and label
Forwarding algorithm is independent of control module
This separation which allows flexibility in control planes also
Enables straightforward adaptation to Lambda switching

## Slide 6: Label Stack
Arbitrary number of labels
Each label is 20 bits
Label Stack Operations
  Push- add a label to the stack
  Swap - replace the top label
  Pop - remove the top label
Allows multiple control components to act on a packet
Traffic Engineering
Unicast Routing
Virtual Private Network
Unicast
Routing
Traffic
Engineering
VPN

## Slide 7: MPLS Control Components
Label Stack enables combinations of Control Planes
Example: VPN service over Unicast Routing
Unicast
Routing
Traffic
Engineering
Differential
Sevices
Frame
Relay
Quality of
Service
(eg RSVP)
Multicast Routing (PIM v2)
Virtual
Private
Networks
Label Information Base (LIB)
Per-Label Forwarding, Queueing, and Multicast
Mechanisms
Many possible control planes
Multiple Control Planes can manipulate labels
Combinations of control planes allow many services
MPLS - Multi-Purpose Label Switching
Notes: While we’ve only described the mechanisms that support the most basic form of Tag Switching - destination based, unicast, tag switching - there are many additional ways that tags can be assigned.
Because tag switching separates the forwarding operation in IP nodes from its reliance on the destination IP address, tag switching provides great flexibility in the algorithms and techniques it supports for mapping tags to packets. Examples include:
Destination prefix
Forwarding Equivalence Classes - This is a generalization of the previous method. When a router receive a packet, it must decide how to forward that packet. All packets forwarded with same way can be said to be in the same FEC and this would form the basis for mapping tags onto packets and determining how to tag switch a tagged packet.
Explicit routing - Packets can be tagged such that they flow along specified routes, allowing network managers to balance the load across trunk circuits between nodes or cope with unbalanced network topologies during a node outage. This is analogous to the use of virtual circuits in pure Layer 2 devices for Internet traffic engineering.
Application Flows - this method looks at both the source and destination address, as well as other Layer 3 information. This can be used to provide finer granularity in processing the tagged packets and maintain a given quality of service through the network for a specific source/destination flow of packets
Multicast - Tags can be assigned based on the IP multicast trees created with protocols like PIM.
QoS - Tags can be assigned to individual RSVP flows, to aggregated RSVP flows, or to differentiated services classes. The tags would then be used by intermediate network nodes to properly queue tagged packets to deliver the required quality of service.
VPNs - both the physical port (or logical port, in the case of frame relay or ATM virtual circuit) on which a packet is received bythe tag edge router, as well as its destination IP address, can be used to assign tags. By defining which ports are in a particular VPN, proper assignment of tags can create a connectionless virtual network between those ports. Since backbone nodes look at tags and not IP addresses when forwarding tagged packets, packets from different VPNs with overlapping address spaces can be accommodated.

## Slide 8: Multiple Control Planes Unicast and VPNs
Data Packet
Two Labels
The outer label identifies the Egress LSR
The inner label identifies the destination VPN
The VPN Control Module applies a VPN Label and determines Egress LSR
The Unicast Forwarding Control Module supplies the Label to route to the Egress LSR
Swap
Pop
Pop
The ingress MPLS Edge Switch or Router pushes two labels on each packet
Push
Push
Similarly, the stack could be a Label and a Lambda

## Slide 9: MPLS: Bringing Layer 2 Benefits to Layer 3
Traffic engineering
  Least cost path may be overloaded
  Establish explicitly routed label switched paths in order to
  Steer packets onto less loaded links
  Result: Optimal link utilization
Route chosen by
IP routing protocol
Route specified by
traffic engineering
FR edge node
Notes: 34
8
So once again the benefits of efficient encapsulations are the ability to
  engineer traffic across you’re backbone leveraging higher utilization and building in redundancy.
  interior route tagging that supports hierarchical routing by limiting the routing information required in the core to only interior routes
  and support for legacy Frame Relay encapsulation across a gigabit IP core.

## Slide 10: Prior to MPLS: Overlay Model
Separate Layer 2 Network (Frame Relay or ATM)
Mike O’Dell
UUnet, November 17, 1996
“The use of the explicit Layer 2 transit layer gives us very exacting control of how traffic uses the available bandwidth in ways not currently possible by tinkering with Layer 3-only metrics.”

## Slide 11: The Overlay Solution
Layer 2 network used to manage the bandwidth
Layer 3 sees a complete mesh
L3
L3
L3
L3
L3
L3
L3
L2
L2
L2
L2
L2
L2
L3
L3
L3
L3
L3
Physical
Logical

## Slide 12: Overlay Drawbacks
More complex network management
  Two-level network without integrated NM
  Multi-home problem
  Additional training, technical support
IGP routing doesn’t scale for meshes
  Number of LSPs generated for a failed router is O(n3); n = number of routers

## Slide 13: An LSP Tunnel
R8
R2
R6
R3
R4
R7
R5
R1
Normal Route R1->R2->R3->R4->R5
Tunnel: R1->R2->R6->R7->R4
Labels, like VCIs can be used to establish virtual circuits

## Slide 14: TE System Block Diagram
Traffic
Engineering
Control
Path
Selection
TE Topology
Database
RSVP
Flooding
Routing
IS-IS/OSPF
TE Link
Adm Ctl
Forwarding Engine

## Slide 15: TE Tunnel Attributes
Bandwidth
Setup & Holding priorities
  Used for Admission Control
Resource class affinity
    Simple policy routing
Path Options
  Input to route selection

## Slide 16: LSP Tunnel Setup
Setup: Path (R1->R2->R6->R7->R4->R9) Tunnel ID 5, Path ID 1
22
49
17
R8
R2
R6
R3
R4
R7
R1
R5
R9
Reply: Reserves bandwidth on each link
Communicates Labels (or Lambdas)
Pop
32

## Slide 17: Path Resilience
Traffic Engineering Control monitors tunnel status
Keeps a “where used” list of network links
Monitors link status from Routing
Monitors RSVP state

## Slide 18: MPLS Advantages
Scalability
  Integrated routing
  Solves N2 problem
Integrated recovery
  Tunnel status notification
Monitors RSVP state
  IP knows state of the real topology

## Slide 19: MPLS Advantages
Flexible backup
Non-disruptive restoration
Simpler system
  Fewer protocols to manage
  Simpler configuration
  Single Network Management

## Slide 20: Basic OTN Requirements
Dynamic reconfiguration / rearrangement
Establish optical channels in real-time
Support traffic engineering functions
support various protection and restoration schemes

## Slide 21: OXC Control Plane Requirements
Resource discovery
Topology state information dissemination
  Reliable broadcast
Path Selection (constraint-based routing)
Connection management (optical channel)
  Path placement
  Path maintenance
  Path revocation

## Slide 22: Proposal
Adapt MPLS Traffic Engineering control plane to OXCs
Framework for real-time provisioning of optical channels
Especially advantageous for IP-centric OTNs
Solves the multi-home problem
Uniform network management and control

## Slide 23: Characteristics of Approach
Supports
  Optical channel bandwidth management
  Real-time provisioning of optical channels
  Versatile protection and restoration capabilities
  Preliminary framework for an Optical Internet

## Slide 24: Further Merits
Exploit MPLS TE control technology
Trivialize control coordination problems
Simplifies hybrid LSR / OXC network administration

## Slide 25: Next Steps
Articulate end-to-end architectural implications
Develop domain specific adaptation functions
Develop interoperable extensions
What are the roles of the IETF & OIForum in this effort?

## Slide 26: From the IETF Side
MPLS wg charter has been extended to include adapting the MPLS control plane to Lambda switching
IETF generally relies on informal liaisons
Best work happens when a subset of interested parties actively participate in both organizations